ANNUAL AVERAGE READING OF WATER FOR THE YEAR 2013

| Sl. No | Parameter | Method Used | Unit | RESULT : River Tlawng, Upstream, Aizawl | RESULT : River Tlawng, Downstream, Aizawl | RESULT: River Tuirial, Upstream, Aizawl | RESULT: River Tuirial, Downstream, Aizawl | RESULT: Ramhlun North Tuikhur, Aizawl | RESULT : Mission Vengthlang Tuikhur, Aizawl |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | 2050 | 2051 | 2052 | 2053 | 2054 | 2055 |
| 1. | Velocity of Flow | Float Method | m/s | 0.6 | 0.62 | 0.88 | 0.85 | 0 | 0 |
| 2. | Water Temperature | Thermometric Method | oC | 23.58 | 23.75 | 23.58 | 23.5 | 19.5 | 19.33 |
| 3 | Dissolved Oxygen | Iodometric Method | mg/l | 7.1 | 6.98 | 7.07 | 6.98 | 4.85 | 2.64 |
| 4 | pH | Electrometric Method |  | 7.5 | 7.61 | 7.88 | 7.82 | 6.63 | 7.53 |
| 5 | Conductivity | Conductometric Method | μs/cm | 189.08 | 196.83 | 229.28 | 174.15 | 164.23 | 218.88 |
| 6 | Biochemical Oxygen Demand | Dilution Method | mg/l | 1.9 | 1.79 | 1.58 | 1.79 | 1.27 | 0.83 |
| 7 | Nitrogen-Nitrite (N-NO2) | Calorimetric Method (Diazotization Method) | mg/l | 0.144 | 0.129 | 0.136 | 0.125 | 0.121 | 0.171 |
| 8 | Total Coliform | Multiple Tube Dilution Technique | MPN |  |  |  |  |  |  |
| 9 | Faecal Coliform | Multiple Tube Dilution Technique | MPN |  |  |  |  |  |  |
| 10 | Alkalinity | Visual Titration | mg/l | 63.69 | 65.85 | 67.65 | 65.66 | 41.28 | 164.63 |
| 11 | Turbidity | Turbimetric Method | NTU | 0.4 | 0.42 | 0.5 | 0.33 | 0.0 | 17.1 |
| 12 | Chloride | Argentometric titration | mg/l | 17.3 | 26.47 | 10.66 | 9.95 | 31.09 | 62.141 |
| 13 | Nitrogen Ammonia (N-NH3) | Calorimetric Method | mg/l | 1.905 | 1.96 | 2.179 | 1.813 | 1.519 | 2.375 |
| 14 | Total hardness as CaCO3 | Complexometric Titration | mg/l | 53.17 | 53 | 55 | 58.36 | 70.83 | 155.4 |
| 15. | Calcium | Complexometric Titration | mg/l | 12.8 | 12.27 | 13 | 14.75 | 17.53 | 40.16 |
| 16 | Magnesium | Calculation Method | mg/l | 5.04 | 5.31 | 5.75 | 5.77 | 6.46 | 11.18 |
| 17 | Total Dissolved Solids | Gravimetric Method | mg/l | 129.17 | 153.33 | 142.5 | 169.09 | 95 | 100 |
| 18 | Total Suspended Solids | -----do----- | mg/l | 66.25 | 73.33 | 75 | 79.09 | 47.5 | 50.059 |
| 19 | Phosphate,PO43- | Calorimetric Method (Stannous Chloride Reduction Method) | mg/l | 0.247 | 0.266 | 0.383 | 0.239 | 0.286 | 17.197 |
| 20 | Sodium | Flame Photometric method | mg/L | 46.5 | 38.3 | 45.3 | 50.13 | 39.4 | 86.2 |