WATER QUALITY DATA UNDER NWMP : ANNUAL AVERAGE - 2012

| Sl. No | Parameter | Method Used | Unit | RESULT : River Tlawng, Upstream, Aizawl | RESULT : River Tlawng, Downstream, Aizawl | RESULT: River Tuirial, Upstream, Aizawl | RESULT: River Tuirial, Downstream, Aizawl | RESULT: Ramhlun North Tuikhur, Aizawl | RESULT : Mission Vengthlang Tuikhur, Aizawl |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Velocity of Flow | Float Method | m/s | 1.25 | 1.24 | 1.06 | 1.19 | 0.0 | 0.0 |
| 2. | Water Temperature | Thermometric Method | oC | 23.58 | 23.58 | 23.58 | 23.58 | 20.5 | 18.83 |
| 3 | Dissolved Oxygen | Iodometric Method | mg/l | 6.54 | 6.33 | 6.5 | 6.93 | 5.18 | 1.91 |
| 4 | pH | Electrometric Method |  | 7.41 | 7.5 | 7.17 | 6.95 | 6.44 | 7.08 |
| 5 | Conductivity | Conductometric Method | μs/cm | 297.63 | 287.23 | 375.96 | 349.28 | 311.25 | 321.08 |
| 6 | Biochemical Oxygen Demand | Dilution Method | mg/l | 0.88 | 0.83 | 1.13 | 1.13 | 0.97 | 0.68 |
| 7 | Nitrogen-Nitrite (N-NO2) | Calorimetric Method (Diazotization Method) | mg/l | 0.132 | 0.141 | 0.171 | 0.185 | 0.145 | 0.255 |
| 8 | Total Coliform | Multiple Tube Dilution Technique | MPN | 438.18 | 204.05 | 622.68 | 508.75 | 331.42 | 624.75 |
| 9 | Faecal Coliform | Multiple Tube Dilution Technique | MPN | 20.72 | 5.38 | 33.79 | 35.12 | 30.6 | 23.28 |
| 10 | Alkalinity | Visual Titration | mg/l | 56.84 | 56.73 | 62.26 | 58.18 | 34.57 | 194.15 |
| 11 | Turbidity | Turbimetric Method | NTU | 8.25 | 10.58 | 10 | 11 | 0.5 | 0.83 |
| 12 | Chloride | Argentometric titration | mg/l | 15.35 | 10.46 | 10.09 | 15.88 | 51.01 | 75.23 |
| 13 | Nitrogen Ammonia (N-NH3) | Calorimetric Method | mg/l | 1.309 | 0.964 | 1.692 | 1.635 | 0.684 | 3.011 |
| 14 | Total hardness as CaCO3 | Complexometric Titration | mg/l | 45.57 | 51.5 | 44.5 | 45.17 | 93.33 | 170.33 |
| 15. | Calcium | Complexometric Titration | mg/l | 12.13 | 12.73 | 9.6 | 9.93 | 27.33 | 47.8 |
| 16 | Magnesium | Calculation Method | mg/l | 4.83 | 4.68 | 4.84 | 4.85 | 5.57 | 12.17 |
| 17 | Total Dissolved Solids | Gravimetric Method | mg/l | 122.5 | 127.5 | 126.67 | 128.33 | 110.67 | 97.5 |
| 18 | Total Suspended Solids | -----do----- | mg/l | 58.33 | 70 | 100.83 | 110.83 | 42.5 | 53.33 |
| 19 | Phosphate,PO43- | Calorimetric Method (Stannous Chloride Reduction Method) | mg/l | 0.201 | 0.223 | 0.386 | 0.362 | 0.249 | 0.771 |
| 20 | Sodium | Flame Photometric method | mg/L | 27.63 | 30.92 | 32.5 | 34.92 | 61.29 | 76.83 |